Single and Multiple Implant Placement Protocall:

I    Implant Stent Fabrication

There are several reasons for fabricating implant stents aside from the obvious—accurate placement in all three dimensions to assure ease of restorability, optimal esthetics, function, cleansibility and longevity, not to mention patient satisfaction.

Often times when making measurements and calculations and subsequently “drilling on the pre-operative model” as a part of stent fabrication, certain issues become apparent that make us more aware of conditions, obstacles, considerations, etc. that will come into play at the upcoming surgery visit.  These include but are not limited to ridge anatomy, relationship of the opposing tooth or  teeth, anatomy of adjacent contact areas, undercuts and propensity for larger than normal (i.e. potential food traps) embrasure areas, lack of interocclusal clearance, location of the muccogingival junction, etc.  This is to say nothing of decrease in operator stress at the time of surgery combined with decrease in treatment time as the path of the pilot drill has been precisely pre-determined.

Steps in Implant Stent Fabrication:

Requirements:

Upper and lower study models (often times, a triple tray impression will suffice and the quadrant models can be mounted on quadrant articulators)

Drill Press (Harbor Freight Drill Presss)

http://search.harbo rfreight.com/cpisearch/web/search.do?keyword=drill+press

1/16” drill bits (1.6mm diameter)

Set of Digital Calipers

Adjustable Surveyor Table       Tubing for Creation of Implant Guide Sleeves

(External diameter of 1.7mm/internal diameter of 1.6mm)  http://store.microgroup.com/materials.cfm

Order item # 304H16X

Pilot Drills from Salvin Dental

(go to:  http://drills-burs.salvin.com/Pilot-Drills.html)